## Slide 1
SUMMER PROGRESS UPDATE
XY Theta Pen Plotter
Notes: [Sources]
- User-provided toolhead CAD render.
- No external assets or claims.

## Slide 2
SUMMER PROGRESS
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
2
MECHANICAL TOOLHEAD
Built and iterated
N20 lead-screw actuator
Spring preload
Load-cell force path
Finalized X Y Theta frame
18” Diameter 720 tooth bed.
CONTROL SPLIT
Ownership definitions
Converter app converts .SVG files to .gcode
iosender sends .gcode to GRBLHAL OS on RP23CNC
RP23CNC owns X/Y/A, M3/M5 motion orchestration.
Pro Micro owns control system(N20 motion, force sensing) and toolhead safety.
COMMISSIONING
Planned
Test definitions for:
Force calibration
Lift-home repeatability
M5 clearance
Interchangeable-tool checks
Finish motor wiring
Progress is being documented as measured tests in TEST_PLAN.md
E – Electrical/Electronics
F – Firmware/Controller
M – Motion
T - Toolhead
Notes: [Sources]
- Internal project architecture, test plan, and user-provided CAD.
- No external assets or claims.

## Slide 3
HIGH-LEVEL ARCHITECTURE
Separating coordinated motion and local force control
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
3
Host PC
SVG → G-code
ioSender streams commands
RP23CNC / grblHAL
Plans X/Y/A motion
Homing and P100 registration
Toolhead Pro Micro
Reads load cell
Controls N20 and safety
Pen + paper
Writing force
creates the mark
→
G-code
→
M3 / M5
→
force
Toolhead control system
Gcode creation
Movement
Notes: [Sources]
- Internal system architecture and interface documents.
- No external assets or claims.

## Slide 4
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
4
INTERFACE PROTECTION
Opto-isolation
Digital paths carry commands and status without sharing grounds.
RP23CNC / controller
Opto-isolation
Pro Micro / toolhead
5 V and ~12 V domain
3.3 V domain
ENA - M3 / M5 (forward/retract)
U1
GP29 - command input
Aux 0 - arm request (homing start)
U2
GP28 - request input
PRB – input signal + encoder
U3
GP27 - status output
Notes: [Sources]
- Internal system architecture and interface documents.
- No external assets or claims.

## Slide 5
HOW THE MACHINE HOMES
Homing: machine position and toolhead touch calibration
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
5
1
P100 requests toolhead-home handshake
RP23CNC sends the existing GP28 request.
→
2
Pro Micro verifies toolhead switch trigger
N20 retracts; the upper switch defines LIFT_HOME.
→
3
Toolhead replies “ready”
Existing GP27 signals success; a timeout becomes a fault.
→
4
RP23CNC homes X/Y
Physical switches
→
5
Magnetic scan registers G54
Center point magnet sets X/Y zero
outer magnet sets A zero.
The toolhead switch remains local to the Pro Micro; the existing GP28/GP27 pair lets P100 receive the result
Retraction for homing safety
Homing movement
Notes: [Sources]
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 6
1. Start command
Command ioSender → RP23CNC: G65 P100 Q0 Decision owner RP23CNC / grblHAL starts P100 locally. Not moved HX711 force samples stay inside the Pro Micro toolhead.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 7
2. Toolhead home
Request P100 asserts GP28. Pro Micro action N20 retracts until GP2 confirms LIFT_HOME. Reply GP27 ready, or a timeout becomes a fault.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 8
3. Machine home
Command RP23CNC runs . Result Physical X/Y switches establish gantry coordinates. Toolhead stays at LIFT_HOME.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 9
4. Magnetic registration
Request / reply GP28 requests the scan; GP27 reports TMAG. Result Center magnet sets G54 X/Y zero. Outer magnet sets A zero.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 10
5. Per-run touch check
M3 Seek down to the load-cell contact threshold. M5 Release, then make a bounded clearance pulse. Abort Fail to touch, release, or clear.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 11
6. Ready state
Ready G54 registered; pen clear of paper. Drawing M3 writes. M5 releases and travels. GP2 is not used for each lift.
1
2
3
Notes: [Sources]
- docs/p100-data-movement.html rendered as a static image.
- firmware/grblhal/HOMING_AND_MAGNETIC_CALIBRATION.md
- No external assets or claims.

## Slide 12
HOW THE MACHINE PRINTS
The print cycle uses force feedback to find paper and maintain pressure
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
7
M3 • engage and write
1. N20 lowers the carriage slowly.
2. Load cell crosses the contact threshold.
3. Controller holds the selected writing force while X/Y/A move.
M5 • release and travel
1. N20 retracts until the load cell says the pen released.
2. A bounded clearance pulse creates an air gap.
3. The machine travels to the next mark without moving to the distant home switch.
The spring provides compliance; the load cell determines pressing versus clear.
Notes: [Sources]
- firmware/pen_pressure/CONTROL_STRATEGY.md
- No external assets or claims.

## Slide 13
NEXT STEPS
Next: toolhead-home step completion
THETA PEN PLOTTER • SUMMER PROGRESS UPDATE
8
E-07
Calibrate load cell
Convert HX711 readings into reproducible force units.
T-01G/H
Verify lift and clear
Prove GP2 homing and repeatable M5 release/clearance.
T-01J
Check writing tool
Touch and clear before every run; pens or pencils.
F-05 / integration
Connect M3/M5
Verify the motion controller and toolhead work together.
Calibration drawing
Adjust system based on calibration results
Measure line quality, force trace, and geometry.
Notes: [Sources]
- docs/testing/TEST_PLAN.md
- No external assets or claims.